## Slide 1: Pipeline
Epochs mean and management
Measures
T test
Correlation
Classification
External statistical analysis
Detailed pipeline

## Slide 2: Pipeline
Epochs mean and management
Measures
T test
Correlation
Sampling Frequency
Input Data
Frequency Bands
Epochs
Subjects
Locations
Output Data
Statistical Data
Correlation Data

## Slide 3: Output Data
Output Data
Statistical Data
Correlation Data
Epochs mean and management
Measures
T test
Correlation
Sampling Frequency
Input Data
Frequency Bands
Epochs
Subjects
Locations
Measures matrices: a measure matrix for every subject output of the "Measures" block (PSDr, connectivity or FOOOFer), which
sizes depends on the measure type, the number of epochs and the number of bands (epochs*locations,
(bands*epochs*locations or bands*epochs*locations*locations)
Group matrices: a measure matrix for every studied group (healthy control, HC, and patient, PAT) output of the "Epochs
mean and management" block, which contains the measure of every subject of the same group, mediated
over the epochs (subjects*locations, subjects*bands*locations, subjects*bands*locations*locations or
subjects*locations*locations)
External matrix: a matrix useful for external studies (classification, statistical analysis, etc) output of the "T test" block,
which joins the computed patterns of the groups, starting by PATs and ending with HCs (subjects*patterns)

## Slide 4: Statistical Data
Output Data
Statistical Data
Correlation Data
Epochs mean and management
Measures
T test
Correlation
Sampling Frequency
Input Data
Frequency Bands
Epochs
Subjects
Locations
Probability matrix: the matrix of the probability of observing the given result, or one more extreme, by chance if the null hypothesis ("medians are equal") is true for each comparation
Significativity matrix: a matrix which contains some information about significative comparations (locations, bands, etc)

## Slide 5: Sampling Frequency
Output Data
Statistical Data
Correlation Data
Epochs mean and management
Measures
T test
Correlation
Sampling Frequency
Input Data
Frequency Bands
Epochs
Subjects
Locations
Sampling Frequency: sampling frequency of the input data

## Slide 6: Locations
Output Data
Statistical Data
Correlation Data
Epochs mean and management
Measures
T test
Correlation
Sampling Frequency
Input Data
Frequency Bands
Epochs
Subjects
Locations
Locations: a matrix which contains the locations (scout for sources data, channels for scalp data), in order as the rows of the
input data matrices

## Slide 7: Epochs
Output Data
Statistical Data
Correlation Data
Epochs mean and management
Measures
T test
Correlation
Sampling Frequency
Input Data
Frequency Bands
Epochs
Subjects
Locations
Number of epochs: number of the epochs to compute for the selected measure
Time period: time window for every epoch to compute
Starting time: starting time of the first epoch to compute

## Slide 8: Input data
Output Data
Statistical Data
Correlation Data
Epochs mean and management
Measures
T test
Correlation
Sampling Frequency
Input Data
Frequency Bands
Epochs
Subjects
Locations
Input Data: a matrix locations*time for each subject to analyze in the study

## Slide 9: Frequency Bands
Output Data
Statistical Data
Correlation Data
Epochs mean and management
Measures
T test
Correlation
Sampling Frequency
Input Data
Frequency Bands
Epochs
Subjects
Locations
Cut Frequencies: an array which contains all the cut frequencies to utilize for each computation (for example, for the Alpha and Beta bands it will be [8 13 30])
Total band: an array which contains the starting and the ending value of the total band used to obtain the relative PSDs computing the PSDr

## Slide 10: Subjects
Output Data
Statistical Data
Correlation Data
Epochs mean and management
Measures
T test
Correlation
Sampling Frequency
Input Data
Frequency Bands
Epochs
Subjects
Locations
Sampling Frequency: sampling frequency of the input data

## Slide 11: Measures
FOOOF
PSD relative
Connectivity
Pipeline

## Slide 12: PSD relative
PSD relative over a total band using the Welch’s power formulation
The function PSDr computes the Power Spectral Density relative over a total band (defined by the user or not) using the Welch’s power formulation.
It saves a 3D matrix named psd (bands*epochs*locations) for each input EEG matrix (locations*time) related to the scalp or to the sources of a folder which contains all and only the EEG matrices.
PSDr(fs,cf, nEpochs,dt,inDir,outDir,tStart, cfstart, cfstop)
fs is the sampling frequency
cf is an array containing the cut frequencies (es, [1 4 8 13 30 40])
nEpochs contains the number of epochs to compute
dt contains the time (in seconds) of each epoch
inDir is the directory containing each case
outDirs are the directories where saving each computation of the respective measure
tStart is the starting time (in seconds) to computate the first sample of the first epoch (0 as default)
cfstart is the index of the first minimum cf value's step to save (1 as default)
cfstop is the index of the last maximum cf value's step to save (length(cf) as default)
relBand is the band used to obtain the relative PSD ([min(min(cf),1) max(max(cf),40)] as default)
PSDr
psd
(bands*epochs*locations)
EEG
(locations*time)
Measures

## Slide 13: FOOOF
Parametrization of the neural power spectrum
The function FOOOFer parameterizes the neural power spectra using the Haller et al. method.
FOOOFer(fs, cf, nEpochs, dt, inDir, outDirs, tStart, outTypes)
fs is the sampling frequency
cf is an array containing the cut frequencies (es, [1 40])
nEpochs contains the number of epochs to compute
dt contains the time (in seconds) of each epoch
inDir is the directory containing each case
outDirs is the list of the directories, written as strings in an array, where saving each computation (for example
["C:\offset\", "C:\exponent"])
tStart is the starting time (in seconds) to computate the first sample of the first epoch
outTypes is the list of variables to save (offset, exponent, peak parameters, gaussian parameters, error, r squared, fooofed
spectrum, bg fit, power spectrum), writen in an array as strings in the same order as their output directories in the variable outDirs (es. outDirs=["C:\offset\", "C:\exponent", "C:\bg_fit"], outTypes=["offset", "exponent", "bg fit"])
FOOOFer
parameters
EEG
(locations*time)
Measures
Peaks
Power spectra
Aperiodic parameters
Goodness of fit metrics

## Slide 14: Aperiodic parameters
Offset: aperiodic broadband offset
Exponent: aperiodic slope
FOOOF

## Slide 15: Goodness of fit metrics
R2 (R squared): coefficient of determination (proportion of the variance in the dependent variable that is predictable from the
independet variables)
RMSD (error): root mean square error (measure of the differences between values predicted by the model)
FOOOF

## Slide 16: Peaks
Peak parameters: oscillations center frequency (CF), power (Amp) and bandwidth (BW) of the original power spectrum
Gaussian parameters: oscillations center frequency (CF), power (Amp) and bandwidth (BW) of the multi-Gaussian model
NB: peak and gaussian params will contain a matrix where every group of 3 numbers are relative to one peak (CF, Amp, BW)
and the others zeros are utilized to export only one matrix for each subject
FOOOF

## Slide 17: Power spectra
Power spectrum: original power spectrum
Background fit (bg fit): aperiodic fit of the power spectrum
Fooofed spectrum: full model fit of the power spectrum
FOOOF

## Slide 18: Connectivity
Pattern of causal interactions (effective connectivity) between distinct units within a nervous system
The function connectivity computes the connectivity between EEG channels or ROIs, using the phase locking value (PLV), the phase lag index (PLI), the amplitude envelope correlation corrected (also called orthogonalized, AECo) or the amplitude envelope correlation not corrected (AEC).
It saves a 3D matrix named conn (bands*epochs*locations*locations) for each input EEG matrix (locations*time) related to the scalp or to the sources of a folder which contains all and only the EEG matrices.
connectivity(fs,cf, nEpochs,dt,inDir,outDirs,tStart, outTypes)
fs is the sampling frequency
cf is an array containing the cut frequencies (es, [1 4 8 13 30 40])
nEpochs contains the number of epochs to compute
dt contains the time (in seconds) of each epoch
inDir is the directory containing each case
outDir is the directory where saving each computation
tStart is the starting time (in seconds) to computate the first sample of the first epoch (0 as default)
outTypes is the list of connectivity types to compute (ex. ["AEC" "AECo" "PLI"])
connectivity
conn
(bands*epochs*locations*locations)
EEG
(locations*time)
Measures

## Slide 19: AEC orthogonalized
Amplitude Envelope Correlation orthogonalized
The function amplitude_envelope_correlation_orth computes the AEC orthogonalized between EEG channels or ROIs.
It takes a matrix time*locations in input and returns a connectivity matrix locations*locations.
AECo=amplitude_envelope_correlation_orth(sig)
sig is the input matrix (in the format time*locations)
AECo is the matrix of the orthogonalized amplitude envelope correlation
amplitude_envelope_correlation_orth
AECo
(locations*locations)
sig
(time*locations)
Connectivity
amplitude_envelope_correlation_orth
Connectivity

## Slide 20: AEC
Amplitude Envelope Correlation
The function amplitude_envelope_correlation computes the AEC between EEG channels or ROIs.
It takes a matrix time*locations in input and returns a connectivity matrix locations*locations.
AECo=amplitude_envelope_correlation (sig)
sig is the input matrix (in the format time*locations)
AEC is the matrix of the amplitude envelope correlation
amplitude_envelope_correlation
AEC
(locations*locations)
sig
(time*locations)
Connectivity
amplitude_envelope_correlation
Connectivity

## Slide 21: PLI
Phase Lag Index
The function phase_lag_index computes the PLI between EEG channels or ROIs.
It takes a matrix time*locations in input and returns a connectivity matrix locations*locations.
PLI=phase_locking_value(sig)
sig is the input matrix (in the format time*locations)
PLI is the matrix of the phase lag index
phase_lag_index
PLI
(locations*locations)
sig
(time*locations)
Connectivity
phase_lag_index
Connectivity

## Slide 22: PLV
Phase Locking Value
The function phase_locking_value computes the PLv between EEG channels or ROIs.
It takes a matrix time*locations in input and returns a connectivity matrix locations*locations.
PLV=phase_locking_value(sig)
sig is the input matrix (in the format time*locations)
PLV is the matrix of the phase locking value
phase_locking_value
PLV
(locations*locations)
sig
(time*locations)
Connectivity
phase_locking_value
Connectivity